## Slide 1
How to Train Your Model
with Project Refinery
Matt Jezyk
Tesla (formerly Autodesk)

## Slide 2
Matt Jezyk
Senior Staff Software Engineer, Tesla
Former Senior Engineering Manager, AEC Generative Design, Autodesk

## Slide 3: A SPECIAL THANKS TO:

## Slide 4: American Institute of Architects (AIA) Continuing Education Services (CES)
Credit(s) earned on completion of this course will be reported to AIA CES for AIA members. Certificates of Completion for both AIA members and non-AIA members are available upon request.
This course is registered with AIA CES for continuing professional education. As such, it does not include content that may be deemed or construed to be an approval or endorsement by the AIA of any material of construction or any method or manner of handling, using, distributing, or dealing in any material or product.
___________________________________________
Questions related to specific materials, methods, and services will be addressed at the conclusion of this presentation.
For AIA accredited sessions only

## Slide 5: Session Description
Creating parametric options is easier than ever, but creating 'good' options is still quite hard. Creating good design options starts by asking the right questions, and then by embedding your custom design logic into code. We will teach you how to code 'Evaluators' and train your model using Project Refinery.
AIA Provider: RTC Events Management LLC Course Number: AIADBW 229
Course Date: July 18, 2019
  At the end of this session, participants will be able to:
  1. Frame a design problem in terms of goals and constraints
  2. Learn how to write psuedocode to help define the logic before writing final code
  3. Develop new custom code in multiple programming languages (Dynamo, DesignScript, Python, and C#)
  4. Test the custom logic in a larger generative workflow
Learning Objectives

## Slide 6
HOW TO USE GENERATIVE DESIGN TOOLS TO ADVANCE ARCHITECTURAL DESIGN PROCESSES.
Notes: This slide can be used to highlight one or two sentences that tie into the topic that you’re presenting on.
For example, if you have an impactful quote or idea that you would like to share, this would be the ideal place to include this message.
Messaging must always be in ALL CAPS to tie into the style and theme.

## Slide 7: Overview
WHY?
HOW: How to define goals and metrics
HOW: Evaluator Examples
  Hill Climbing – What’s an Objective Function?
  Massing Study – Real-World Goals Made Into Evaluators
  Solar Analysis – Using Simulation Results
  Desk Layout – More Evaluators
Questions

## Slide 8: Example files are all Open Source!
The examples for this class:
  https://github.com/tatlin/BiLT_NA_2019_How_To_Train_Your_Model
Refinery Primer:
  https://refineryprimer.dynamobim.org/
  https://github.com/DynamoDS/RefineryPrimer
Refinery Toolkit Dynamo Package and Examples Files:
  https://github.com/DynamoDS/RefineryToolkits
Thank You To Our Partners:
  DesignTech/ENSTOA, ProvingGround, and Autodesk Research

## Slide 9: Why?

## Slide 10
Notes: We know that by 2050 there will be 10 billion of us.
What we might not all know is that the global middle class is growing faster than at any time in our history.
In 1990, only 23% of the global population had sufficient income to be classified as middle class. Today, 45% of us do.

## Slide 11
13,000
BUILDINGS A DAY
30x
AROUND THE EARTH / PER YEAR
Notes: Recently Autodesk partnered with a firm called Statista to calculate just how much work …
<click>
We’re going to have to build 13,000 buildings every day
<click>
And enough roads and rail to wrap around the earth six times every year …
That’s over 1.2 million km of roads and rail needed for our global infrastructure each and every year between now and 2050

## Slide 12: Problem: more work at a higher quality with less resources
Notes: I’m going to assert that there is a problem
Most people just evaluate a few designs, generative design can let you study much more.

## Slide 13
Notes: This has been the traditional way of delivering buildings
Recording it on paper and delivering it to others who execute to build it
We've evolved to computerizing drawings making them more data rich and easier to updated

## Slide 14
Notes: But what we really want to do now is to capture what’s in these people’s heads

## Slide 15
Professional Intelligence
Algorithmic Opportunity
Notes: Combine intelligence of building professional with algorithmic intelligence to produce better buildings, faster.

## Slide 16
Notes: We are also doing experiments with these workflows inside of Autodesk.
Recently, we moved our Toronto office to a new office in the MaRS innovation district. The Living, an architecture firm that Autodesk purchased to test out ideas, used a generative approach to design the new office’s space layout.

## Slide 17
Notes: They boiled all this data down to six measurable goals for a good office and created algorithms to measure each goal.

## Slide 18
Notes: To generate viable space plan proposals reliable results, the Living created a series of formulae to arrive at optimal solutions…

## Slide 19
Notes: To generate viable space plan proposals reliable results, the Living created a series of formulae to arrive at optimal solutions…

## Slide 20
Notes: To generate viable space plan proposals reliable results, the Living created a series of formulae to arrive at optimal solutions…

## Slide 21
Notes: Here you can see the process running, as different floor plan layouts are created, each with blue amenity bars of meeting rooms and yellow locations of desks.
Each design option also involves a “dashboard” of performance according to its score on the six goals.

## Slide 22
Notes: They set up variables so that designers could flex them to see what the effects of the variables are.
They generated 10s of 1000s of options, developed methodology to sort through them and help them make decisions.

## Slide 23
Notes: Autodesk Research and The Living also worked on a project with the Dutch construction company Van Wijnen. In this project they followed a similar workflow where they identified certain goals, developed ways to measure those goals, developed a flexible model, and used the computer to help generate, evolve, and rank their designs.

## Slide 25: “We want to be able to learn from more designs than it is physically possible to generate or evaluate ‘by hand’.” – Danil Nagy, The Living
Notes: the outcome of the search is completely dependent on the design of the design space, as well as the specification of various measures and search parameters. So you do you design a good design space?
Some things to keep in mind…

## Slide 26: How!?

## Slide 27: What is Project Refinery?
Automatically run Dynamo created logic to create options
Works on Dynamo for Revit or Dynamo Sandbox
Created for one customer VanWijnen 2/2018
Public Beta 11/2018

## Slide 28
autodesk.com/solutions/refinery-beta

## Slide 29: Generative Design Preparation
How to get started
Understand what you want to achieve
Define your problem
Decide on ways to measure success
Think about how to review the results
Notes: The traditional architectural design process is similar to the generative design process in many ways. In the traditional architectural design process, you ask for requirements from your client – how big a building do you want? What kinds of spaces to you need in the building? What goals do you have for the design?
This traditional process of identifying goals and requiements is still important when incorporating generative design techniques. With generative design you usually can’t design all aspects of a building in one automated process, you have to identify what kinds of problems might be good to look at in ways that the computer can help you to generate options and evaluate them. But you are still defining goals and measuring success. It’s critical to design how the problem with be generated by the computer and how you will measure success. How are you going to make decisions on the results?

## Slide 30: Traditional Design Process
Notes: Traditional Design process is a little bit like a game of battle ship. Ideas are tested one at a time. “does this work?” “what about this?” You might get a hit, you might get a miss. Often times only a few designs can really be evaluated because you run out of time. Solutions presented on cost only when you really want to show the client more options.

## Slide 31: Generative Design Process
PEOPLE
Refinery generates iterations on your behalf
Evaluate
Curate
Detail
Concept
Constraints
Goals
COMPUTER
PEOPLE

## Slide 32: “The goal of generative design is not to automate the design process, or to replace human designers with artificial ones” – Danil Nagy, The Living
Notes: the outcome of the search is completely dependent on the design of the design space, as well as the specification of various measures and search parameters. So you do you design a good design space?
Some things to keep in mind…

## Slide 33: Generative Design Method
Process diagram
Notes: How is your model going to flex to create different options?
How are you going to measure success?
How do other options compare?
How can the computer help you to generate options to evolve your design to the best design for your goals?
How can you visualize the results ---- and explain the best options to your clients?
Once you decide on a direction, how can you integrated it into other programs for further work?

## Slide 34: 3 Box Building Let’s start simple to understand concepts
Example 1
Notes: Be sure to always include a title and a subhead

## Slide 35: Goals
Study a building mass to look at trade offs between volume and surface area
Variable Inputs:
  Locations of 2 of the boxes
  Heights of all 3 boxes
Goals:
  Maximum volume (rentable area)
  Minimum surface area (expensive façade)
What are we solving for?

## Slide 36: Quick Dynamo Primer
Visual programming for architects and engineers

## Slide 37
INPUTS
GEOMETRY
EVALUATORS
Notes: Types of inputs

## Slide 39
Notes: Pink box inputs
Green box geometry creation
Critical to define how the geometry flexes.

## Slide 41
Input types
VARIABLE
FIXED
REFINERY
Notes: Types of inputs

## Slide 42: Generate
How you parametrize the model is critical
Too many inputs will lead to a design space that is too big to explore
Too few inputs won’t yield a big enough design space
Create a design system: 3 key concepts
Notes: Human process

## Slide 43
Optimize
Cross Product
Randomize
Like This
Refinery Generation Methods

## Slide 44: Refinery Methods
INPUTS
DESIGN SPACE
OUTCOME
4 TYPES
RANDOMIZE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations/ good for testing the model
Like this · to apply slight variations to your current input configuration
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 45
4 TYPES
RANDOMIZE
INPUTS
DESIGN SPACE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
OUTCOME
5 DESIGNS
# defined by user
Refinery Methods
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations
Like this · to apply slight variations to your current input configuration
ntelligence methods
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 46
4 TYPES
RANDOMIZE
CROSS PRODUCT
INPUTS
DESIGN SPACE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
OUTCOME
5 DESIGNS
# defined by user
Parameter 1
Parameter 2
5x
3x
Parameter 1
Parameter 2
5 x 3 = 15 DESIGNS
user defines sampling density
Refinery Methods
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations
Like this · to apply slight variations to your current input configuration
intelligence methods
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 47
Parameter 1
Parameter 2
4 TYPES
RANDOMIZE
CROSS PRODUCT
OPTIMIZE
INPUTS
DESIGN SPACE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
OUTCOME
5 DESIGNS
# defined by user
Parameter 1
Parameter 2
5x
3x
Parameter 1
Parameter 2
5 x 3 = 15 DESIGNS
user defines sampling density
population of 3
generation 1
Parameter 1
Parameter 2
Refinery Methods
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations
Like this · to apply slight variations to your current input configuration
intelligence methods
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 48
Parameter 1
Parameter 2
4 TYPES
RANDOMIZE
CROSS PRODUCT
OPTIMIZE
INPUTS
DESIGN SPACE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
OUTCOME
5 DESIGNS
# defined by user
Parameter 1
Parameter 2
5x
3x
Parameter 1
Parameter 2
5 x 3 = 15 DESIGNS
user defines sampling density
population of 3
generation 1
…
population of 3
generation 2
population of 3
generation 6
3 x 6 = 18 DESIGNS
user defines population size and number of generations
Parameter 1
Parameter 2
Refinery Methods
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations
Like this · to apply slight variations to your current input configuration
intelligence methods
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 49
Parameter 1
Parameter 2
4 TYPES
RANDOMIZE
CROSS PRODUCT
OPTIMIZE
LIKE THIS
INPUTS
DESIGN SPACE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
OUTCOME
5 DESIGNS
# defined by user
Parameter 1
Parameter 2
5x
3x
Parameter 1
Parameter 2
5 x 3 = 15 DESIGNS
user defines sampling density
population of 3
generation 1
…
population of 3
generation 2
population of 3
generation 6
3 x 6 = 18 DESIGNS
user defines population size and number of generations
Parameter 1
Parameter 2
Parameter 1
Parameter 2
Parameter 1
Parameter 2
Refinery Methods
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations
Like this · to apply slight variations to your current input configuration
intelligence methods
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 50
Parameter 1
Parameter 2
4 TYPES
RANDOMIZE
CROSS PRODUCT
OPTIMIZE
LIKE THIS
INPUTS
DESIGN SPACE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
OUTCOME
5 DESIGNS
# defined by user
Parameter 1
Parameter 2
5x
3x
Parameter 1
Parameter 2
5 x 3 = 15 DESIGNS
user defines sampling density
population of 3
generation 1
…
population of 3
generation 2
population of 3
generation 6
3 x 6 = 18 DESIGNS
user defines population size and number of generations
Parameter 1
Parameter 2
5 DESIGNS
# defined by user
Parameter 1
Parameter 2
Parameter 1
Parameter 2
Refinery Methods
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations
Like this · to apply slight variations to your current input configuration
intelligence methods
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 51
Notes: Can quickly create random options

## Slide 52
Notes: But we need something to guide our study

## Slide 53
Critical 2nd half of the problem
Set of measures that determine how the building is performing
Why?
  Compare designs objectively (apples to apples)
  Evaluate designs based on non-intuitive measures
  Explore more designs than is possible manually
Judging outcomes
85%
91%
94%

## Slide 54
Types of measurement
COMPLEX
Simulation
SIMPLE
length x width=area
UNMEASURABLE
BEAUTY
PERSONAL PREFERENCE
AESTHETIC SENSIBILITY
Notes: Goals here were to study building forms with most volume and least surface area (measurable)
Could add more complex measurement types like solar radiation if I wanted to measure that…
But also aesthetic preferences among those designs (unmeasurable)

## Slide 55
Types of measurement
Notes: Goals here were to study building forms with most volume and least surface area (measurable)
Could add more complex measurement types like solar radiation if I wanted to measure that…
But also aesthetic preferences among those designs (unmeasurable)

## Slide 56
Measuring goals
Notes: Types of inputs

## Slide 57
Designating Refinery inputs and outputs
Notes: Types of inputs

## Slide 59: 3. Rank
Refinery sort
Notes: Compare designs that fulfil our design goals by sorting by Surface Area and then Volume

## Slide 60: 3. Rank
Manual "optimization"
Notes: Using the built in graph functionality you can compare these metrics against eachother and filter to find the compromise options that meet both goals.

## Slide 61: 3. Evolve

## Slide 62
  Output goals
  Population size
  Generation size
  Seed
Parameters that effect the algorithm
Notes: We are parametrically setting nsga2 settings like mutation rate and cross over chance. The values change based on number of inputs and input range.

## Slide 63
Refinery optimization

## Slide 64
Refinery randomization vs. optimization
40 random runs – 10 sec
100x100 optimization – 4 min
Notes: Show pareto front with “utopia point”, sped up video of designs coming and going, evolving to better options
Explain pareto front – surface area and volume example
  Compare random run graph to optimized run (thinner front line)
  Sort for max volume and then min surface area

## Slide 66
Refinery Explore UI

## Slide 68
Notes: Types of inputs

## Slide 70: 2D Hill Climbing Let’s go back a step and focus on goal-setting and how to make evaluators
Example 2 (or 0)
Notes: Be sure to always include a title and a subhead

## Slide 71: Goals
Find Maximum Height Z for Point P
Variable Inputs:
  Curve C
  Point P
Goals:
  Maximum Height Z
What are we solving for?
Curve C
Max Height Z
Point P

## Slide 72: Goals
Curve C
Max Height Z
Point P
Find Maximum Height Z for Point P
  z = f(c,p)
  maximize z
Variable Inputs:
  Curve C
  Point P
Objective Function:
  z = f(c,p)
  Find maximum height
  f(c,p) =
    Projected Point P’ = P.Project(C)
    Height Z = P’.z
    x = P.x
What are we solving for?

## Slide 73
Curve C
Max Height Z
Point P
INPUTS
GEOMETRY
EVALUATORS
  Projected Point P’ = P.Project(C)
  Height Z = P’.z
  x = P.x

## Slide 74
EVALUATORS
Measuring goals
Notes:   f(c,p) =
    Projected Point P’ = P.Project(C)
    Height Z = P’.z
    x = P.x

## Slide 76
Parameter 1
Parameter 2
TYPES
RANDOMIZE
OPTIMIZE
INPUTS
DESIGN SPACE
Parameter 1
Parameter 2
Parameter 1
Parameter 2
OUTCOME
5 DESIGNS
# defined by user
population of 3
generation 1
…
population of 3
generation 2
population of 3
generation 6
3 x 6 = 18 DESIGNS
user defines population size and number of generations
Parameter 1
Parameter 2
Refinery Methods
Notes: Deterministic methods
Save · an individual option by editing input values on Refinery
Cross-product · to survey the whole design space
Randomize · to obtain random input configurations
Like this · to apply slight variations to your current input configuration
intelligence methods
Optimize · a set of output parameters of a parametric model to improve the performance of your design

## Slide 77
INPUTS
Parameter 1
Parameter 2
Parameter 1
Parameter 2
5 DESIGNS
# defined by user
Refinery Methods
TYPES
RANDOMIZE

## Slide 81
MORE INPUTS!

## Slide 82
INPUTS
Refinery Methods
TYPES
OPTIMIZE
Parameter 1
Parameter 2
population of 3
generation 1
…
population of 3
generation 2
population of 3
generation 6
3 x 6 = 18 DESIGNS
user defines population size and number of generations
Parameter 1
Parameter 2

## Slide 84
INPUTS
Refinery Methods
TYPES
OPTIMIZE
Parameter 1
Parameter 2
population of 3
generation 1
…
population of 3
generation 2
population of 3
generation 6
3 x 6 = 18 DESIGNS
user defines population size and number of generations
Parameter 1
Parameter 2

## Slide 86
Find Maximum Height Z for Point P
  z = f(c,p)
  maximize z
Variable Inputs:
  Curve C
  Point P
Objective Function:
  z = f(c,p)
  Find maximum height
  f(c,p) =
    Projected Point P’ = P.Project(C)
    Height Z = P’.z
    x = P.x
Measuring goals – DesignScript

## Slide 87
Measuring goal - Python

## Slide 90: Local Solver – More Advanced Evaluator
Python loop to move points closer to local peaks
  Position y = f(x) position function we have been using
  Tangent dy = f’(x)dx f’(x) is the derivative of x
  Slope/Velocity v = dy/dx slope of tangent line represents ‘velocity’
  Acceleration dv = f’’(x) change in slope of tan line is ‘acceleration’
Global Solver vs Local Solver
f’(x) = (f(x + h/2) - f(x - h/2))
h

## Slide 91: Newton’s Method in Python

## Slide 95: Building Massing
Example 3
Notes: Be sure to always include a title and a subhead

## Slide 96: Goals
Retail and office distribution and configuration for a building on an urban site.
Variable Inputs:
  1. Ratio retail to office
  2. Program block size
  3. Program block rotation
Goals:
  1. Minimize zoning envelop overlap
  2. Minimize cost
  3. Maximize total value per year
What are we solving for?

## Slide 97
INPUTS
GEOMETRY
EVALUATORS
INTEGRATORS

## Slide 103: Metric Comparison
Building Massing Study
Metric | Retail | Office
Cost Per SF | $180 | $300
Floor to Floor Height | 14 | 15
Revenue/SF/YR | $35 | $25
Elevation Bonus (0-50’) | 1 | 1
Elevation Bonus 51-150’ | 0.25 | 1.2
Elevation Bonus 151’+ | 0.1 | 1.5
Orientation Bonus 0-20 | n/a | 1
Orientation Bonus 21-40 | n/a | 1.2
Orientation Bonus 41+ | n/a | 1.5

## Slide 109: Refinery
40 Random Runs
Least Value/Yr
Notes: Lots of retail high up, less office means less value per year

## Slide 110: Refinery
40 Random Runs
Most Value/Yr
Notes: Retail on bottom floors, more office for more value per year

## Slide 111: Refinery
40 Random Runs
Lowest Cost
Notes: More retail, less expensive to build

## Slide 112: Refinery
40 Random Runs
Highest Cost
Notes: More office, more expensive to build

## Slide 113: Refinery
40 Random Runs
Medium Cost
Medium Value

## Slide 114: Refinery
40 Random Runs
Medium Cost
Medium Value
Lowest volume
Outside zoning

## Slide 116: Refinery
20x50 Optimization
Medium Cost
Medium Value
Lowest volume
Outside zoning
Notes: More similar options, fill up zoning boundary (?)

## Slide 117: Adding New Evaluator to Building Massing
Example 3.5
Notes: Be sure to always include a title and a subhead

## Slide 118: StealthyRoofScapes!

## Slide 119: Re-using and Re-applying Evaluators

## Slide 122: StealthyRoofScape Evaluator On Building Massing

## Slide 123: Solar Analysis
Example 4
Notes: Be sure to always include a title and a subhead

## Slide 125: Office Layout
Example 5
Notes: Be sure to always include a title and a subhead

## Slide 126: Goals
Look at desk layouts that gives us the most desks but also the most private desks while maximizing desk area per person and minimizing unutilized space.
Variable Inputs:
  Edge to start layout
  Desk rotation
  Position on room surface
  Desk clearance
  End offset
Goals:
  Maximize number of desks
  Maximize desk area per person
  Maximize space utilization
  Maximize number of private desks
What are we solving for?

## Slide 127
INPUTS
GEOMETRY
EVALUATORS
INTEGRATORS

## Slide 133
How far is it from desk to desk?
How many desks are less than 12’ away from each other?
How many desks have less than 3 desks within 12’?

## Slide 134: Refinery
40 Random runs
Most Private Desks
Most Desks

## Slide 136: Refinery
10x20 Optimization
Most Private Desks
Most Desks

## Slide 139: Refinery Primer Samples
Example 7 – Overflow Samples
Notes: Be sure to always include a title and a subhead

## Slide 140: Autodesk MaRS Office
Example 10 – Overflow Samples
Notes: Be sure to always include a title and a subhead

## Slide 141: Tiling
Example 11 – Overflow Samples
Notes: Be sure to always include a title and a subhead

## Slide 142: Refinery Beta Samples
Example 12 – Overflow Samples
Notes: Be sure to always include a title and a subhead

## Slide 143: A SPECIAL THANKS TO:

## Slide 144: REMINDER Speaker and Session Feedback is Appreciated
Go to Sessions
Select this Session
Select Session Rating

## Slide 145: Reference Links
https://refineryprimer.dynamobim.org/
  https://refineryprimer.dynamobim.org/02-getting-started/02-01_anatomy-of-a-good-generative-design-process
  https://refineryprimer.dynamobim.org/06-using-revit-alongside-refinery/06-03_detailed-example-workflow
https://github.com/DynamoDS/RefineryPrimer
https://www.keanw.com/
  https://www.keanw.com/2019/06/project-rediscover-is-now-available-for-download.html
https://dynamobim.org/math-transit/ 2d point plotting
https://scipy-lectures.org/advanced/mathematical_optimization/index.html
https://en.wikipedia.org/wiki/Numerical_differentiation
https://aroberge.blogspot.com/2005/04/computing-derivatives-using-python.html

## Slide 146: REMINDER Session materials are available on the Conference App
Session 1.5 How to Train Your Model with Project Refinery
Matt Jezyk

## Slide 147: Visit me at the Speaker Lounge
I will be at the Speaker Lounge outside the Exhibition Hall for further conversations. Please join me there at this time:
Thursday 18 (06:10 PM - 08:10 PM)
Or at the Exhibition Networking Function that evening

## Slide 148: Questions?
How to Train Your Model with Project Refinery
Matt Jezyk, Senior Staff Software Engineer, Tesla
Formerly Senior Engineering Manager
Autodesk AEC Generative Design
@MattJezyk